## Slide 1: Location-aware Traffic Offloading
Quoc-Nam Le-The
Systems and Computer Engineering Department
Carleton University

## Slide 2: Motivation
Offload cellular traffic to small cells, D2D communications, and Wi-Fi without routing through mobile access and core network.
Achieve this by using location estimation to classify users for local caching of data for traffic offloading.

## Slide 3: Overview
Use NNSS (nearest neighbor(s) in signal space) to estimate the location of users (Location estimation may not be needed)
Use kNN to classify the users
Use classifications to offload traffic to nominate candidate AP (local devices) for traffic offloading/caching

## Slide 4: Location Estimation
Off-line Phase – determine the location and orientation of the user that best matches a set of signal space measurements.[1]
  The signal space measurements can either be gathered during the off-line phase or determined using signal propagation modelling.
  Measuring during the off-line phase becomes more time consuming as the covered area increases.
Use NNSS (nearest neighbor(s) in signal space) to determine the location and orientation that best matches the observed signal strengths.
  NNSS computes the average location of the k nearest neighbors in signal space and assigns the location to the user.

## Slide 5: User Classification
Use kNN to classify the user.
  Each access point (or users) has a classification.
  The user computes the k nearest neighbors based on received signal strength (the stronger the signal the “nearer” they are).
  Of the k nearest neighbors classify the user with the classification that is in the majority.
    May use weights to limit the effect of locations with high density of users (give users less weight than small cells for classification).

## Slide 6: Caching
Small cells cache the data ahead of time.
  How to determine what data should be cached ahead of time?
    Content based of popularity
    Location based content (Live video feed from an event)
Users that classify with the small cells download and cache the data from the small cells and other users with the same classification.
  Who do you download from?
    Access points with the strongest received signal strengths and same classification?
    How to distribute the load? Should the users contribute less than the small cells?